## Slide 1: Write a program to copy the values 55H into RAM memory locations 40H to 45H using direct addressing modes, Register indirect addressing modes
MOV A,#55H
MOV 40H,A
MOV 41H,A
MOV 42H,A
MOV 43H,A
MOV 44H,A
MOV A ,#55H
MOV R0,#40H
MOV @R0,A;40H(add)=55H
INC R0
MOV @R0,A;41H(add)=55H
INC R0
MOV @R0,A ;42H(add)=55H
INC R0
MOV @R0,A ;43H(add)=55H
INC R0
MOV @R0,A ;44H(add)=55H

## Slide 2: Instruction set:
Arithmetic &logical
Code 8051assembly language programming

## Slide 3: Arithmetic instructions
Unsigned numbers
Unsigned numbers are defined as data in which all the bits are used to represent data
00-FF (0-255)

## Slide 4: Additions of Unsigned Numbers
In the 8051 ,in order to add numbers together , the accumulator register must be involved
Instruction ADD is used to add two operand
Destination operand must be A register
Source operands can be register, immediate data or in memory
ADD A, source ; A= A + Source

## Slide 5: 3C E7 +3B 8D 77 74
E7
+ 8D
74
MOV A , #E7H
ADD A , #8DH; A = 74H
3C
+3B
77
MOV A,#3C
ADD A, #3B ; A = 77H

## Slide 6: 1 3C E7 +3B 8D 78 74
When adding two 16-bit data operands , concerned of propagation of carry from lower byte to higher byte
ADDC A, Source ;A= A + Source+1
MOV A,#E7
ADD A ,#8D;A=A+8D
MOV R0, A
MOV A ,#3C
ADDC A ,#3B; A=A+3B+1
MOV R1, A