## Slide 1: Timers/Counters
List the timers of the 8051 and their associated registers
Describe the various modes of the 8051 timers
Program the 8051 timers
Program the 8051 counters

## Slide 2: Timers/counters
8051 has two timers.
They can be used either as timers to generate a time delay or as counters to count events happening outside the microcontroller.

## Slide 3: Basic registers of the timer
Both timers 0 and timers 1 are 16 bit wide
Since the 8051 has an 8 bit architecture each 16 bit timers is accesses as two separate registers of two low byte and high byte.

## Slide 4: Timers 0 registers
The 16 bit register of timers 0 is accessed as low byte and high byte.
The low byte registers is called TL0 and high byte registers is referred as TH0
These registers can be accessed like any other registers such as A,B,R0 R1 etc.MOV TL0,#40H

## Slide 5: Timer 1
The 16 bit register of timers 0 is accessed as low byte and high byte.
The low byte registers is called TL1 and high byte registers is referred as TH1

## Slide 6: TMOD (timers mode) Register
Both timers 0 and 1 use the same registers called TMOD to set various timer operation modes.
TMOD is an 8 bit registers in which the lower 4 byte are set aside for timer 0 and upper 4 bits for timer 1.
4 byte :lower 2 bits are used to set the timer mode and upper 2 bits to specify the operation

## Slide 8: C/T(clock timers)
This bit in the TMOD registers is used to decide whether the timer is used as a delay generator or an event counter.
If C/T=0 ,it is used as a timer for time delay generation
The clock source for the time delay is the crystal frequency of the 8051 .

## Slide 9: GATE
Every timer has a means of starting and stopping
Achieved by software /hardware in 8051
The start and stop of the timer are controlled by way of the software by the TR bits TR0 and TR1 ex.SETB TR1 ,CLR TR1
These instructions start and stop the timers as long as GATE=0 in the TMOD registers.

## Slide 10: MODE1
It is 16 bit timer (0000-FFFF) to be loaded into timers registers TL and TH.
The timers must be started . SETB TR0 for timer 0
It start to count up until it reaches its limits of FFFFH.When it roll over from FFFFH to 0000H ,it set high a flag bit called TF .This timer flag can be monitored and stop the timer by CLR TR0
In order to repeat the process the registers TH and TL must be reloaded with the original value and TF must be reset to 0.

## Slide 11
LOAD the timer
Start the timer
Monitored the timer
Stop the timer
Reset the TF bit before reload

## Slide 12: Create a square wave with a 50% duty cycle on the P1.5bit Timer 0 is used to generate the time delay
MOV TMOD,# 01
MOV TL0, #0F2H
MOV TH0,#0FFH
CPL P1.5
ACALL DELAY
SJMP HERE
DELAY: SETB TR0
JNB TF0,AGAIN
CLR TR0
CLR TF0
RET
AGAIN:
HERE:
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6