## Slide 2: Overview
A microcontroller is a small and low-cost microcomputer, which is designed to perform the specific tasks of embedded systems like Washing machine, displaying microwave’s information, receiving remote signals, etc.
The general microcontroller consists of the processor, the memory (RAM, ROM, EPROM), Serial ports, peripherals (timers, counters), etc.

## Slide 3: Difference between Microprocessor and Microcontroller

## Slide 5: Applications of Microcontrollers
Microcontrollers are widely used in various different devices such as −
Light sensing and controlling devices like LED.
Temperature sensing and controlling devices like microwave oven, chimneys.
Fire detection and safety devices like Fire alarm.
Measuring devices like Volt Meter.

## Slide 6: What is an 8051 Microcontroller?
The 8051 microcontroller was invented in 1980's by Intel.
Its foundation is based on Harvard architecture and this microcontroller was developed principally for bringing it to be used in Embedded Systems.
It is an 8-bit microcontroller.
It is built with 40 pins DIP (dual inline package)

## Slide 7: Features of 8051 Microcontroller
It having four register banks
64K bytes on-chip programmable memory (ROM)
128 bytes on-chip data memory (RAM)
Address bus is 16-bit unidirectional
Data bus is 8-bit bidirectional
128 user defined flags
16 bit timers (2 timers)
32 general purpose registers each of 8-bit
32 I/O pins
8051 microcontroller offers a number of special features such as ADC, UARTs, Op-amp, etc.

## Slide 8: 8051 Microcontroller Architecture

## Slide 9
In the following diagram, the system bus connects all the support devices to the CPU.
The system bus consists of an 8-bit data bus, 16-bit address bus and bus control signals.
All other devices like program memory, ports, data memory, serial interface, interrupt control, timers, and the CPU are all interfaced together through the system bus.

## Slide 10: CPU
CPU act as a mind of any processing machine.
It synchronizes and manages all processes that are carried out in microcontroller.
User has no power to control the functioning of CPU.
It interprets the program stored in ROM and carries out from storage and then performs it projected duty.
CPU manage the different types of registers available in 8051 microcontroller.

## Slide 11: Interrupts
Interrupts is a sub-routine call that given by the microcontroller when some other program with high priority is request for acquiring the system buses then interrupts occur in current running program.
Interrupts provide a method to postpone or delay the current process, performs a sub-routine task and then restart the standard program again

## Slide 12: Memory
Why 8051 Microcontroller need memory?
For operation Micro-controller required a program.
This program guides the microcontroller to perform the specific tasks.
This program installed in microcontroller required some on chip memory for the storage of the program.
Microcontroller also required memory for storage of data and operands for the short duration.
In microcontroller 8051 there is code or program memory of 4 KB that is it has 4 KB ROM and it also comprise of data memory (RAM) of 128 bytes.

## Slide 13: System Bus
Bus is a group of wires which uses as a communication canal or acts as means of data transfer. The different bus configuration includes 8, 16 or more cables. Therefore, a bus can bear 8 bits, 16 bits all together
Address Bus:8051 microcontrollers is consisting of 16 bit address bus. It is generally be used for transferring the data from Central Processing Unit to Memory.
Data bus:8051 microcontroller is consisting of 8 bits data bus. It is generally be used for transferring the data from one peripherals position to other peripherals.
Control bus:

## Slide 14: Oscillator
As the microcontroller is digital circuit therefore it needs timer for their operation.
To perform timer operation inside microcontroller it required externally connected or on-chip oscillator.
Microcontroller is used inside an embedded system for managing the function of devices. Therefore, 8051 uses the two 16 bit counters and timers.
For the operation of this timers and counters the oscillator is used inside microcontroller.