## Slide 1: Serial data communication and programmable communication interface
The serial data transmission is always preferred for long distance transmission.
Why ?
How ?
But…….

## Slide 2
It requires software
SOD / SID
RIM SIM But……….

## Slide 4: Programmable communication Interface
Many types of Universal asynchronous receiver transmitter and Universal synchronous / asynchronous receiver transmitter have been developed for data transfer between serial I/O devices and microprocessor.
It provides programmable serial communication interface between microprocessor and serial I/O devices.
The data transfer between microprocessor and USART is take place in parallel form.
The data transfer between USART and I/0 devices is take place in serial form.
The USART has to be initialized before the data transfer takes place.
The desired data formats and synchronization method for the data transfer are specified during initialization by command byte written by the microprocessor for the USART.

## Slide 5: PIN diagram of 8251

## Slide 6: Block diagram of 8251
How many different sections does 8251 have?
The functional block diagram of 8251 is shown in figure. It includes following four sections:

## Slide 7
Read / Write control logic
Transmitter sections
Receiver sections
Modem control
Data bus buffer

## Slide 8: How the 8251 is programmed? Control Register
This is 16-bit register and contains the control word with two independent bytes.
The first byte is called the Mode instruction word and second byte is called command instruction word.
This register can be accessed as an output port when C/D(bar) pin is high.

## Slide 9: Read /Write control logic
This section includes six input
signals CS,RD,WR,C/D,CLK,RESET
& three buffer registers
Control register
Status register
Data bus buffer register

## Slide 10
CS(bar):It is a chip select terminal. A low signal to this terminal selects the 8251A for communication with the microprocessor. This is connected with decoded address bus.
C/D(bar): It is a control /data pin. A high on this terminal addresses the control register or status register; where as low addresses the data bus buffer.
WR(bar):It is a active low write signal. When a low signal is applied to this terminal, the microprocessor either writes in the control word register or send the output to the data buffer. This pin is connected to either IOW/MEMW(bar)
RD(bar):It is an active low read signal. When this terminal low, the microprocessor either read the status from the status register or accepts the data from data from data buffer. This pin is connected to either IOR/MEMR(bar)
RESET: It is a RESET input pin. When this terminal is high, it reset the 8251 and force it in the ideal mode.
CLK:This is clock input, usually connected with system clock

## Slide 11: What is the function of the Status Word Register of 8251? Status register
This input register checks ready status of a peripheral. This register is addressed as an input port when c/D(bar) is high. It has same port address as control word.

## Slide 12: Data Bus buffer register
This is a bidirectional address and can be addressed as an input port and output port when C/D bar pin is low.

## Slide 14: Transmitter section
It consist of following three registers:
  Transmitter buffer register: It holds 8-bit data
  Serial output register: Converts 8-bit into a stream of serial bits
  Transmitter control Logic: It directs the output register to send the serial data at the output register through TxD lines.
Three output pins and one input pins

## Slide 15
TxD: It is a transmit data terminal. The serial bits are transmitted on this lines.
TxC(bar):This pin is Transmitter clock. This control the rate at which bits are to be transmitted by the 8251A.The clock frequency can be 1,16 or 64 times of baud.
TxRDY(bar):This is transmitter ready pin. When this output terminal is high it indicate that the buffer is empty and 8251 is ready to accepts a byte. This signal becomes reset when the data byte is loaded into the transmitter buffer register.
TxE:This is transmitter empty signal used as output signal. A high on this terminal indicates that output register is empty and becomes reset when a byte is transferred from the buffer register to the output register.

## Slide 16: Receiver section
Function of receiver section?
The receiver section accepts serial data on the RxD terminal and converts it to parallel data.
RxD:It is a receiver data terminal. The serial bits are received on this line and converted to parallel bytes in the receiver input register.
RxC(bar):This pin is receiver clock. This control the rate at which the bits are received by the 8251A.In synchronous mode clock is set to 1,16,64 times of baud .
RxRDY:This is receiver ready pin. When this output pin is high ,8251 has character in the buffer register and ready to transfer it to microprocessor. It can either be used as status to the microprocessor.

## Slide 17: Modem Control
DSR(bar):This is an active low input terminal used by the modem to indicate that it is ready for communication.
CTS (bar):This active low input terminal is used by modem to signal the DTE that communication channel is clear and it can send out the serial data
DTR(bar):This output signal is used by 8251 to signal the modem to indicate that the terminal is ready to communicate.
RTS(bar):This output signal is used by the 8251 to signal to modem that it has data to be transmitted.