## Slide 2: 8051 INTERRUPT
What is Interrupt:
What is ISR: Interrupt subroutine program
What is IVT: Interrupt Vector table

## Slide 3: Steps in executing an interrupt
When an interrupt gets active, the microcontroller goes through the following steps −
The microcontroller closes the currently executing instruction and saves the address of the next instruction (PC) on the stack.
It also saves the current status of all the interrupts internally (i.e., not on the stack).
It jumps to the memory location of the interrupt vector table that holds the address of the interrupts service routine.
The microcontroller gets the address of the ISR from the interrupt vector table and jumps to it. It starts to execute the interrupt service subroutine, which is RETI (return from interrupt).
Upon executing the RETI instruction, the microcontroller returns to the location where it was interrupted. First, it gets the program counter (PC) address from the stack by popping the top bytes of the stack into the PC. Then, it start to execute from that address.

## Slide 4: Six interrupt in the 8051
When the reset pin is activated, the 8051 jumps to the address location 0000. This is power-up reset.
Two interrupts are set aside for the timers: one for timer 0 and one for timer 1. Memory locations are 000BH and 001BH respectively in the interrupt vector table.
Two interrupts are set aside for hardware external interrupts. Pin no. 12 and Pin no. 13 in Port 3 are for the external hardware interrupts INT0 and INT1, respectively. Memory locations are 0003H and 0013H respectively in the interrupt vector table.
Serial communication has a single interrupt that belongs to both receive and transmit. Memory location 0023H belongs to this interrupt.

## Slide 6: Enabling the interrupt
Steps 1) Bit D7 of the IE register must be set to high to allow the rest of register to take effect.
Steps 2) If EA=1, interrupt are enabled and will be responded to if their corresponding bits in IE are high. If IE=0, no interrupt will be responded

## Slide 8: Programming timer interrupt