## Slide 1: Control Word Register
This register is accessed when lines A0 & A1 are at logic 1.
It is used to write a command word, which specifies the counter to be used, its mode, and either a read or write operation.

## Slide 2
After power-up, the state of the 8254 is undefined. The Mode, count value, and output of all Counters are undefined. How each counter operates is determined when it is programmed. Each counter must be programmed before it can be used. Unused counters need not be programmed. Counters are programmed by writing a Control Word and then an initial count.
The format of Control Word of 8254 is:
SC1 | `SC0
0 | 0
0 | 1
1 | 0
1 | 1
M2 | M1 | M0
0 | 0 | 0
0 | 0 | 1
X | 1 | 0
X | 1 | 1
1 | 0 | 0
1 | 0 | 1
RW1 | RW0
0 | 0
0 | 1
1 | 0
1 | 1
SELECTION
C0
C1
C2
Read back status
SELECTION
Counter Latch Command
Read/Write lower byte
Read/Write higher byte
Read/Write lower byte followed by higher byte
OPERATING MODE
MODE 0
MODE 1
MODE 2
MODE 3
MODE 4
MODE 5
BCD/ Binary | 
0 | Binary
1 | BCD

## Slide 3: Counters
Each counter consists of a single, 16 bit-down counter, which can be operated in either binary or BCD. Its input and output is configured by the selection of modes stored in the control word register. The programmer can read the contents of any of the three counters without disturbing the actual count in process.

## Slide 4: Programming the 8254
Why ?: The 8254 can be programmed
1) To provide various type of output through write operations
2) To check a count while counting through read operations
Write operations:
To initialize a counter following steps are necessary
1.Write a control word into control register.
1 0 1 1 0 0 0 0 = BOH
2.Load the lower order byte of a count in the counter register
3.Load the higher order byte of a count in the counter register

## Slide 5: Program:
MVI A,BOH
OUT 83H ; A7 A6 A5 A4 A3 A2 A1 A0
1 0 0 0 0 0 1 1 =83H
MVI A,LOWBYTE;
OUT 82H; A7 A6 A5 A4 A3 A2 A1 A0
1 0 0 0 0 0 1 0 =82H
MVI A,HIGHERBYTE;
OUT 82H;
With a clock and appropriate gate signal to one of the counters start the counters and provide appropriate output

## Slide 6: Program: Read operation:
READ:MVI A,80H ;1 0 0 0 0 0 0 0
OUT 83H
IN 82H
MOV D,A
IN 82H
ORA D
JNZ READ

## Slide 7: Modes of 8254

## Slide 8: MODE 0: Interrupt on Terminal Count
The output becomes a logic 0 when the control word is written and remains there until NUMBER OF PROGRAMMED COUNT.

## Slide 10: MODE1: Programmable one shot
The gate input trigger the counter to output o for count clock.
Counter reloaded if G is pulsed again.

## Slide 12: MODE 2:Rate Generator
Counters generates a series of pulses 1 clock pulse wide.
The separation between pulses is determined by the count
The cycle is repeated until reprogrammed or gate pin set to 0

## Slide 14: Write instruction to generate pulse every 50mcroS from Ctr0

## Slide 15: Mode 3:Square wave generator
Generates a continuous square wave with G set to 1.
If count is even,50% duty cycle otherwise OUT is high 1 cycle is longer.

## Slide 17: Write instruction for 1Khz square wave at Ctr 1

## Slide 18: MODE 4 :Software triggered strobe
Software triggered one shot(Gate must be 1)
OUT goes initially high,it goes low for one clock at the end of count
The count must be reloaded for subsequent output.

## Slide 20: MODE 5:Hardware Triggered Strobe
Hardware triggered is one shot
It is triggered by rising edge at the gate
Initially the OUT is low and Gate triggered from low to high the out HIGH
OUT goes low for one clock period